## Slide 1: ATS Slice Plugin
Coming to a cache near you!
Evan Zelkowitz
(actual work done by Brian Olsen)
A.K.A. Variable Range Requests at Comcast

## Slide 2: Range: bytes=573741824-573888888 Rfc7233 (Range Requests)

## Slide 3: Vanilla cache (ATS, nginx, etc)
Caching proxy will fetch the entire asset from the beginning
Will serve this request when the asset is finally cached.

## Slide 4: The sad story:
The client leaves.
The fetch cancels.
Next client request starts the cycle again.

## Slide 5: Solutions - Background Fetch
ATS plugin background_fetch.so (and background fill)
Incoming client request kicks off a full asset fetch.
Asset is fetched in the background independent of client connection state and ends up fully cached.
Clients can range request off cached data.
Assets can be manually precached before release.

## Slide 6: Solutions - Background Fetch
BUT….
All clients that come in before the fetch is complete leave empty handed.
A single large asset is cached on a single cache stripe.
  Speed, eviction, etc.

## Slide 7: Solutions - Cache Range Requests
Incoming range requests are issued to the origin and are cached.
Cache blocks may be spread across a second level cache group.

## Slide 8: Solutions - Cache Range Requests
BUT…
Each range request is its own cache key.
Range: bytes=0-1023, Range: bytes=0-1024
Only works for very well behaved clients who block their requests

## Slide 9: Solutions - HLS/MPEG-DASH
Origin pre processes audio/video files into small transferrable chunks defined using a manifest.
BUT...
Depends on the origin maintainers.
Not an answer to software releases, patches, updates.

## Slide 10: Solutions - nginx
Has had support for range caching since Dec 2015.
Can be used in concert with ATS to better handle range requests.
Currently used to slice ranges into blocks and assemble them into client responses, allowing ATS to handle caching via the cache_range_requests plugin

## Slide 11: Range slicing/large assets today
ATS -> nginx -> ATS(s) cache_range_requests (dash)
Background fetch (343 remap rules on our third party content)
Cache Range Requests: Comcast specific video

## Slide 12: Slice Plugin
Breaks an incoming request (range or full asset) into multiple byte aligned cacheable block requests.
Re-assembles the block content into client responses.
Block size can be tuned.
Handles both naive audio/video files and large file assets (releases, updates, patches, etc)

## Slide 13: Slice Plugin - Challenges
CDN software excels at data caching and header manipulation/authentication.
CDN isn’t supposed to manipulate content.
CDN software typically fetches, caches and serves SINGLE requests.

## Slide 14: Slice Plugin - Implementation
Borrows concepts from nginx (Dec 2015)
  Only make GET requests.
  When in doubt, GET request first slice block.

## Slide 15: Slice Plugin - Implementation
ATS plugins primarily designed around One to One (one request from client -> one request to parent)
The extended content manipulation “Transform” plugin type works based on One to One interaction.

## Slide 16: Slice Plugin - Implementation
Slice plugin designed around “Server Intercept” handler.
Designed to allow ATS to act as an origin (HTTP server).
  Enables one to many requests.
Lose access to the ATS state machine including:
  Cache management.
  Conditional requests.
  Parent handling (proxying).

## Slide 17: Slice Plugin - Implementation
Cache Range Requests
Handles parent interaction.
Handles block caching.
Handles conditional headers.
Is proven in production.
Lets ATS do what it does best.

## Slide 18: Slice Plugin - Implementation
Server intercept handler takes over.
State machine only consists of data buffer signals.
  Client request ready to read.
  Client request has more data to read.
  Server response ready to read.
  Server response has more data to read.
  Client wants more data….

## Slide 19: Slice Plugin - Implementation

## Slide 20: Slice Plugin - Implementation
Any irregularities need to be handled by the plugin
Past end of data (but inside last block) 416 responses.
Server aborts (passthru)
Subsequent block errors from server (close connection)
Client timeouts and aborts (finish server fetch)

## Slide 21: Slice Plugin - Implementation
Currently 1466 LOC
Includes ATS integrated unit tests of range utility code using the “catch” framework.

## Slide 22: Slice Plugin - Usage
Remap line: test
map http://ats/ http://parent/ @plugin=slice.so @pparam=blockbytes:1m
Blockbytes also supports 512k, 5m, etc.

## Slide 23: nginx remap
map http://example-dash.3rdparty.com/ http://3rdparty-dash-in-loopback.example.net:81/
@plugin…………….. @plugin=tslua.so @pparam=/opt/trafficserver/etc/trafficserver/3rdparty_range_request_manipulation.lua (handles some client oddities of how they request ranges)
map http://3rdparty-dash-out-loopback.example.net/ http://3rdparty-dash-cname.example.net/ @plugin=……. @plugin=cache_range_requests.so

## Slide 24: Slice Plugin - Usage
map https://example.3rdparty.com/ http://3rdparty-dash-cname.example.net/
@plugin=tslua.so @pparam=/opt/trafficserver/etc/trafficserver/3rd_party_range_request_manipulation.lua @plugin=slice.so @pparam=blockbytes:1000000 @plugin=cache_range_requests.so

## Slide 25: Slice Plugin - Usage
Runs through matched remap rule.
Slice plugin takes over and makes a virtual connection back into ATS per slice block using Pristine Url (and modified meta data and range).
Runs through the same remap rules again, skips slice plugin (due to slice header) then runs cache_range_requests.so

## Slide 26: Slice Plugin - Testing
Memory leaks!
Valgrind (single requests, small blocks)
  Also useful for slow ATS testing.
  Compare against simpler plugin for setup leaks.
Jemalloc (data loading)
  Somewhat useful for ATS managed memory.
  Compare against simpler plugin for leaks.

## Slide 27: Slice Plugin - Testing
Stress testing: Origin
Apache httpd
  Fast, known content.
  Custom plugin for fake content lacks in deterministic verifiable content.

## Slide 28: Slice Plugin - Testing
Functional testing:
Custom origin.
Able to generate deterministic data based on header.
Able to simulate positional and block failures.
curl http://ats/~param/~s.2M/&~param/" -H "Range:bytes=999999-1049100"

## Slide 29: Slice Plugin - Testing
Functional testing: Client
Curl
  Conditional headers
  Expected failures (416s, etc)
Grove (golang based ram cache, part of ATC)
  Integration test script and tool written by Jan Van Doorn.

## Slide 30: Slice Plugin - Testing
Stress testing: Client
Rangegetter.go
  Multiple cpus, random range walking
  Mode to verify content using parallel origin request.
rangegetter edgeedge.txt 1999999 4999999 10000 16

## Slide 31: Slice Plugin - Testing
Stress testing: rangegetter.go + custom origin
Ran rangegetter in request only mode.
Turned off ATS caching.
Running on lab server (dual sandy xeon, 192GB ram)
Sustained ~40gigabit/second, cpu limited by client and origin.

## Slide 32: Slice Plugin - Testing
Stress testing: Traffic duplication tester
Good for reliability testing.
Good to check cache compatibility with current nginx solution.
Added md5sum support, ran queries in parallel against a production server for comparison.

## Slide 33: Slice Plugin - Testing
Production testing:
test-3rdparty-server.comcast.net (Fake fqdn  )
Currently running 3rdparty-dash only traffic.
Running for multiple weeks
Slow creep of RES memory
  44.4G Friday, 44.9G Monday ~24 cpu hours

## Slide 34: Slice Plugin - Issues
Cache invalidation
  First block of each request is used to determine cache age and to evaluate any conditional headers.
Calling back into ATS is inelegant
  Manual Cache management as a plugin is HARD.
  ATS smartly manages the virtual callback.

## Slide 35: Slice Plugin
https://github.com/apache/trafficserver/pull/4054/
Thanks!
Happy Birthday Vijay!